## Slide 1: Medical Applications of radiation physics
Riccardo Faccini
Universita’ di Roma “La Sapienza”

## Slide 2: Outlook
Introduction to radiation
  which one ?
  how does it interact with matter?
  how is it generated?
Diagnostics and nuclear medicine:
  Diagnostics (radiography, SPECT, PET,…)
  Molecular radiotherapy
  Radio-guided surgery
Particle beams in medicine
  Radiotherapy
  hadrotherapy

## Slide 3: Introduction to radiation
Which one ?
How does it interact with matter?
How is it generated?

## Slide 4: Radiation of interest
Neutral particles:
High penetration before interacting
Gamma rays: produce electrons
Neutrons: produce low energy protons  more “aggressive”
positrons: positrons annihilate with e- and produce 2 photons that escape patient and interact outside
Other charged particles (electrons, protons, ions):
low penetration, short path, depending on energy
Notes: Perche’ irradia?

## Slide 5: gamma- matter interactions
Gamma rays
  Photoelectric effect
    Emission of electron with same energy as impinging photon
  Compton scattering
    Only part of the energy is transferred to an electron
       photon “remnant” with lower energy and different direction
  Pair production
  gg e-e+ (only if Eg>2me)
Ee
Eg

## Slide 6: gamma-matter interactions (II)
A photon survives unchanged until it interacts  then it transforms
Photon beam attenuates exponentially
N(x)=N(0)e-mx =N(0)e-nsx
m=coefficiente di attenuazione
s=sezione d’urto
n= # atomi per unita’ di volume
stot=s(p.e.)+
s(compton)+
s(pair)

## Slide 7: Charge particles-matter interactions
Dominant interaction: ionization
 continuous release of energy until particle stops
ionized electron

## Slide 8: positron-matter interactions
In 80% of the cases there are two back-to-back mono-energetic photons

## Slide 9: Accelerators: LINAC
Used in medicine for electrons up to few MeV

## Slide 10: Accelerators: CYCLOTRON
Used to accelerate protons/ions
10-30 MeV for radio-isotope production
Up to 200 MeV for radio-therapy
230 MeV Protons

## Slide 11: Accelerators: syncrotrons
Accelerate protons/carbons for therapy up to 4800 MeV

## Slide 12: Medical accelerators

## Slide 13: Radio-isotopes
Unstable nuclei that decay with strong interactions
Produced:
by strong reactions (bombardment of stable nuclei with protons)
as remnants from reactors

## Slide 14: Diagnostics and Nuclear Medicine
Diagnostics (radiography, SPECT, PET,…)
Molecular radiotherapy
Radio-guided surgery

## Slide 15: Diagnostics
Two major categories:
  Morphologic: sensitive only to densities
    Radiography
    TAC
    ultrasound, …
  Functional: sensitive to organ functionalities
    PET
    SPECT
    …

## Slide 16: Diagnostics: radiography
X-rays produced with a cathodic tube by Bremsstrahlung
Interaction between matter and patient
X-ray detection
X-rays
Notes: Pani

## Slide 17: Diagnostics: Tomography
Generic mathematical tool from 1D  2D
CT with X-rays is most renown
Radon transform
Filter
From image to sinogram

## Slide 18: Radio-nuclides for imaging
Administer, to patient (either systemically or locally) a drug which:
  the tumor/organ of interest takes up significantly more than the rest.
  is linked to a radio-nuclide that emits particles via nuclear decay
Wait for the drug to diffuse
Measure the emitted radiation and obtain information

## Slide 19: Diagnostics: SPECT
Inject radionuclide (typically 99Tc but also 131I)
Decays with single photon
Detection ~50cm from source with anger camera
Gamma decays
Single Photon Emission Computerized Tomography
Notes: Pani

## Slide 20: Diagnostics: PET
Inject radionuclide (18F in FDG, FET, 11C in methionine, choline)
b+ decay
Detect the two gammas in coincidence outside patient
Beta+ decays
Positron Emission Tomography

## Slide 21: Radio-guided surgery
Administer, before operation to patient (either systemically or locally) a drug which:
  the tumor takes up significantly more than the healthy tissue.
  is linked to a radio-nuclide that emits particles via nuclear decay
Wait for the drug to diffuse to the margins of the tumor
Start operation
  Remove the bulk of the tumor
  Verify with a probe that detects the emitted particles the presence of:
    Residuals
    Infected lymph nodes

## Slide 22: Radioguided surgery
Three approaches
Gamma: well established, e.g. sentinel lymph-node
Beta+: based on the dual probe approach
Beta-: future fronteer
probe

## Slide 23: radiomethabolic/Brachitherapy
Inject/ position radionuclide (e.g. 131I)
Beta- decays
Electrons release energy in tumor locally
Beta- decays

## Slide 24: Physics Building Blocks of Diagnostics
Nuclear decays
Production of radiation source:
  X rays
  Radio-nuclides  nuclear reactions/accelerators
Dosimetry
Detectors for photons and electrons

## Slide 25: Radiotherapy
From conventional to Hadrotherapy

## Slide 26: Radiotherapy
Goal:
Deliver energy on tumor cells in order to break them in an irreparable way
Large dE/dx
 DNA breaks irreparably
Moderate dE/dX
 chemical reaction due to free radicals

## Slide 27: Conventional radiotherapy
Beam
Photon beams on patient
Large release of energy outside tumor
tumor
Healthy brain
Depth[mm]
beam
Depth

## Slide 28: Radiotherapy LINAC

## Slide 29: Conventional radiotherapy
Photon beams on patient
Large release of energy outside tumor
Multiple beams each of smaller energy (IMRT)
Beam
Depth[mm]
beam
Depth
Notes: Spiegare meglio IMRT

## Slide 30: Hadrontherapy
Proton/ion beams on patient
Concentrate release of energy inside tumor due to release of energy in ionization.
Beam
Depth[mm]
beam
Depth

## Slide 31: Comparison 12C vs IMRT
Better confinement of energy release
More effectiveness in killing cells

## Slide 32: Accelerators
Required proton/Carbon energy
p/C Energy(MeV/u)
Bragg Peak depth (mm)
100/200
160/300
190/350
Proton Kinetic Energy between 100-250 MeV
Carbon Kinetic Energy between 200-400 MeV/u
Notes: Manca GSI

## Slide 33: Accelerators for hadrotherapy

## Slide 34: Present of hadrotherapy

## Slide 35: HT:Monitoring the dose
Why is so crucial to monitor the dose in hadrontherapy ? Is like firing with machine-gun or using a precision rifle..
A little mismatch in density by CT sensible change in dose release

## Slide 36: Measuring the dose
Based on nuclear reactions between the projectile and the patient
Possible nuclear reactions
Don’t exit patient
No detectable signal
Reactions of interest
b+ decays
Prompt g
Charged products
Notes: Mechanism for charged production?

## Slide 37: Physics in Medicine
Nuclear decays
Particle-matter interactions
Particle accelerators
Radiation detection
Radio Isotopes

## Slide 38: PHYSICS IS BEAUTIFUL …
… AND USEFUL
(U. Amaldi)