## Slide 1: The ZDD data structure
Each ZDD channel produces a positive “waveform”, one 8-bit sample every 2 ns
This waveform is then splitted in “fragments”: a sequence of contiguous data samples, each one above a given threshold
Each “cluster” gives a maximum (biggest sample, for calorimetric analysis to come) and a time for this maximum (used in this analysis)

## Slide 2: The ZDD data structure
This time is relative to the start of the ZDD data buffer, so (indirectly) to L1*, that closes the buffer
Only the first part of the buffer, 1600 ns, is analyzed. The second part is thrown away.
L1*
L1*-8200ns

## Slide 3: Finding the ZDD signal timing
The ZDD is sensitive to most of the BEPCII beam crossings. There is much background!
We must maximize the probability of a hit in the ZDD
In addition to the radiative Bhabha selection we require:
  A “strong” missing photon: Emiss>0.4 GeV
  A low emission angle: |cos(θγ)| > 0.98

## Slide 4
ZDD bottom half
ZDD top half
The red histogram shows ZDD “fragment times” (16 ns/bin) when the missing photon points to the ZDD side (cos(θγ) > 0.98)
The black histogram shows ZDD “fragment times” when the missing photon points to the other side (cos(θγ) <- 0.98)
There is a clear accumulation around +200 ns in both plots, FWHM 40-50 ns wide

## Slide 5
ZDD bottom half
ZDD top half
The same plot, zoomed (2ns/bin) on the interesting region.

## Slide 6
Here we correct the timing by subtracting the BESIII “Event start time”, the time scale is again 2ns/bin
The event-to-event variation of the L1* latency is removed
Both peaks are much narrower, and the time shift is because the L1* trigger cable enters the ZDD “bottom” FADC first
The widths (not gaussian, 16ns) are due to the FADCs “trigger sensing” granularity
ZDD bottom half
ZDD top half

## Slide 7: Countercheck 1
The same plot, for the “bad” control sample 0.8 < |cos(θγ)| < 0.97

## Slide 8: Countercheck 2
The same plot, for a “bad” FADC time window, starting at -7200ns before L1*

## Slide 9: Conclusions
We have demonstrated that accumulations of ZDD hits correlate strongly with 2 BESIII subsystems:
  The MDC because the accumulation depends on the polar angle of the missing photon
  The TOF because the timing is made more precise by using the event t0
Also, we have shown that if we shift the trigger window, the correlation vanishes

## Slide 10: Outlook for the 2014-2015 run
The ZDD start of the time window appears correct
The time window will be shortened to 400 ns from 1600much more tolerable for DAQ
The ZDD signal will become part of the BESIII DQM, and will be monitored by ZDD people to make sure that it does not move