h mass measurement
blessing of the final result
Biagio Di Micco

---
Motivation
GEM is in good agreement with old measurements
The most precise
measurements differ by 8s
GEM result:
M = (547.311 ± 0.028 ± 0.032) MeV/c2
Reaction used: p + d → 3He + 
High discrepancy with NA48!
Using 3 from p → n :
M = (547.843 ± 0.030 ± 0.041) MeV/c2
[A, Lai et al., Phys. Lett. B 533 (2002) 196]

---
Method and selection.
 f  hg (h gg)
 f  p0g (p0 gg)
h mass
p0 mass
3g final state
A kinemati fit is performed imposing energy-momentum conservation and time of flight of photons
the energy momentum conservation imposes 4 constraints
the energies of the three photons are over constrained and determined by the angles through the kinematic fit.
c2 < 35
Selection
At least 3 photons with the requirements:
|t – r/c | < min(5st,2ns)
50 < qg < 130
the kinematic fit is performed on all combinations and that with the smallest c2 is retained.

---
Measurement method
constraints equation
energy-momentum conservation
t-r/c of clusters
measured quantities
cluster position x,y,z
cluster energies
cluster times
from e+e-  e+e-
86000 ev./run
s
momentum
vertex position
after kin. fit
before kin. fit
s = 3 MeV/c2
s = 3 MeV/c2
s = 39 MeV/c2
the kinematic fit squeeze the distribution because of the very good angular resolution.

---
Dalitz plot
The photons are ordered according their energies
DATA
c2 < 35
E1 < E2 < E3
p0
 cut
h
signal region
p0 cut
Accepted region

---
Fit of the gg invariant mass
Fit to the invariant mass distribution
DATA
MC
double gaussian for p0
single gaussian for h

---
systematic checks
Cuts
Dalitz plot cut
     c2
photon angle dependence
   azimuthal and polar angle;
vertex position
vertex position determination;
    DC – EMC global misalignment
calorimeter energy response
energy scale knowledge
deviation from linearity
ISR effect on sqrt(s)

---
Dalitz cut systematic
The cut on the Dalitz produces a small distortion on the invariant mass distribution that shifts the measured mass.
The distortion is null in the limit of infinite resolution and can be easily corrected using MC.
The effect is evaluated using a toy MC that just generate h decays with a gaussian mass spectrum with s(DATA)

---
Dalitz cut correction - slope
Toy MC Dalitz
corrected
200 keV
variation
12 keV
residual systematic
DATA
m
MeV

---
Dalitz cut correction - constant
12 keV systematic
rms of the points without correction.
mh
MeV

---
p0 case
Slope cut
4 keV
Constant cut
1.9 keV
Mp MeV
Mp MeV
Mp MeV

---
c2 cut

---
Vertex position and DC-EMC alignment
A sample of p+ p- g has been used to determine shifts in the vertex position and displacement between DC and EMC.
The p+ p- vertex is compared with that coming form e+ e-  e+ e- .
The tracks are extrapolated from the vertex to the calorimeter, and compared with the cluster position.
g
p-
p+
p+
p+ p- g selection criteria
Minimum approach point
50° < qp, qg < 130°
Trackmass, and of the likelihood
p+ p- p0 rejection through kinematic fit

---
Mis-determination of the I.P
We keep the vertex from the tracking algorithm and compare it with the BPOS values event by event
2 normal dist.
2 normal dist.
1 normal distr.
xppg - xeeee
yppg - yeeee
zppg - zeeee

---
displacement as a function of run n.
2001
2002
The standard deviation respect to the zero value is taken as systematic

---
 2002 EMC-DC displacement
z
y
x
p+
p-
Correction applied

---
Vertex+alignment systematic

---
Mass versus vertex position

---
Mass ratio versus vertex position
Uncertainty on the mass values (fractional error)

---
Angular dependence
The 3 photons are boosted back in the f rest frame.
The normal to the plane of the 3 photons is evaluated.
y
f
q
normal
photon plane
15 keV rms
10 keV rms

---
Energy response
The same ppg sample can be used to check the energy response of the calorimeter, comparing the g energy evaluated from the pp tracks with the
cluster energy.
Eclu = 0.994xEtrue – 0.2 MeV
linearity deviation are 2% at most.
Applying these correction we find:
energy scale dm/m = 810-6 (4 keV)
lin. dev. dm/m = 710-6 (4 keV)
Not blessed
Different approach using f p+ p- p0 (p0 gg)
The same result in the overlapping region
(different g energy allowed by the kinematics)

---
Global check of the method
To check possible distortions due to the algorithm itself.
Mfit = Minput + (41 ± 3) keV/c2
 c2/n.d.f = 0.32
50pb-1 for each point
linearity is perfect.
A correction for the constant term is needed.
mh fit
MeV

---
Fit pulls checking
x,y,t ok
z,E difficult to correct.
DATA
MC

---
Dummy simulation
A dummy simulation has been performed that uses GEANFI for vertex simulation and photon transport up to calorimeter: we take the photo conversion point coordinate and then apply a smearing using the following resolution values:
{%sigma_t} = sqrt{(54 ps)^2 over {E(GeV)} + (140 ps)^2}
{%sigma_z} = {0.9 cm} over sqrt{E (GeV)}
{%sigma E} over E = 0.057 over sqrt{E GeV}
{%sigma_x} = 3.4 over sqrt{12} cm { } {%sigma_y} = 2.81 over sqrt{12} { } cm

---
Fit pulls dummy simulation

---
ISR correction and systematics
Due to the ISR the average s of the hg system is lower than the s of the beams.
The difference between the two can induce a correction of 100 keV on the value of the h mass.
To determine the correction and the systematic:
1) we evaluate the correction using the dummy MC as a function of s;
    2) we divide the DATA in s bins and correct for the MC curve, the spread in the corrected value is taken as systematic.

---
ISR correction and systematics h
MC
Corrected values
DATA
The c2/9 = 2.2 sISR = 0.008 MeV
mmean = 547.779  0.005 MeV
Scale factor S = c2 = 1.5

---
ISR correction and systematics p0
MC
Corrected values
DATA
The c2/9 = 1.07 sISR = 0.004 MeV
mmean = 134.874  0.004 MeV
Scale factor S = c2 = 1

---
Systematic summary
p

---
DATA quality filtering
2001-2002 separation line
Period with large s instability have been discarded from the analysis.

---
h mass fit
Each selected value of the mass, is corrected event by event for the evaluated MC ISR correction and put in the histogram. Then the histogram is fitted.
The DATA have been divided in 8 periods.

---
p0 mass and mass ratio fit

---
Fit results
        Using mp0 = 134976.6 ± 0.6 keV (PDG06)
        we obtain
        mh= 548140 ± 50stat. ± 190syst. keV

---
Final value
From the f line shape fit we obtain:
The ratio with the CMD-2 (1019.483 ± 0.011stat ± 0.025syst value sets the absolute scale of our √s measurement.
        We obtain:
1.4 s from PDG

---
Conclusions
0.6 s from NA48
1.4 s from CLEO
 11 s from GEM

---
Fit quality (data sample divided in 8 periods)
h
p0

---
Fit results

---
sqrt(s) correction
The mass shows an high sensitivity to the sqrt(s) value.
dmh/mh ×10-3
dmp/mp×10-3

---
sqrt(s) determination
The absolute scale of the s is obtained fitting the cross section e+e-  KsKL (f line shape).
The fit takes into account the ISR effect and the phase space factor of the KK couple.
mf (CMD-2) = 1019.483±0.011±0.025 MeV
The ratio mf (CMD-2)/mf (KLOE) is used to set the absolute s scale.

---
sqrt(s) not affected estimate:
DPDG = 1s

---
p0gg 2005
434 pb-1
Using the Br evaluated on 2002 data.
½ 2005 statistics 600 pb-1
1s signal
bkg
Br(h®p0gg) = (8.4  2.7stat  1.4syst)  10-5
m(hp0gg)
MC shape from rad04

---
Results and systematics
KLOE PRELIMINARY
the energy calibration has been determined using p+p-g and e+e-g events,
the calorimeter calibration is know at better than 2%
 dm/m = 1110-6 (6 keV) on the  mass.
radiative return and threshold effects included in the fit
Systematic due to the vertex position determination have been also evaluated, the sqrt(s) is calibrated by fitting the f line shape.
m(f) = 1019.483 ± 0.011 ± 0.025
CMD-2 Phys. Lett. B578, 285
M(0) = ( 134990  6stat  30syst ) keV
M(0)PDG = ( 134976.6  0.6 ) keV
M() = ( 547822  5stat  69syst ) keV
NA48 compatibility: 0.24 
Independent measurement with the 
decay mode in progrees:
mh= 547.95  0.15 MeV/c2
(very preliminary fully in
agreement with the gg channel)

---
Results and systematics
KLOE PRELIMINARY
Systematic due to the vertex position determination have been also evaluated, the sqrt(s) is calibrated by fitting the f line shape.
m(f) = 1019.483 ± 0.011 ± 0.025
CMD-2 Phys. Lett. B578, 285
M(0) = ( 134990  6stat  30syst ) keV
M(0)PDG = ( 134976.6  0.6 ) keV
M() = ( 547822  5stat  69syst ) keV
Systematics dominated by √s knowledge
NA48 compatibility: 0.24 
Cross check with → decay mode:
mh= 547.95  0.15 MeV/c2