## Slide 1
QCAL upgrade status
Situation before upgrade
Efficiency, resolution
Background occupancy
Electronic noise
Hardware upgrade
PM replacement
Electronic upgrade
E. Santovetti
Scientific Committee – 29 May 2003

## Slide 2
E. Santovetti
KLOE - 29 May 2003
Efficiency
MIP detection Efficiency vs ch
(efficiency of the single channel !)
Average MIP efficiency = 97 %
Photon efficiency from
KL  +-0 (70 MeV) ~ 85 %
QCAL A
QCAL B

## Slide 3
E. Santovetti
MIP signal amplitude
bad PM
MIP signal amplitude vs ch #
ADC counts
ch. number
After HV equalization the response
remains very inhomogeneous
The Magnetic field (0.52T along axis)
reduces the signal amplitude by 60%
KLOE - 29 May 2003

## Slide 4
E. Santovetti
MIP signal amplitude/2
E(MeV)
E(MeV)
E(MeV)
E(MeV)
QCAL A
Ch. 9
QCAL B
Ch. 9
QCAL A
Ch. 8
QCAL B
Ch. 11
bad channel
The threshold
(3 Ped  or 50 ADC counts)
cuts evidently the signal !
good channel
The signal is "far" from the threshold
KLOE - 29 May 2003

## Slide 5
E. Santovetti
Efficiency
1-eff.
1/Amp. (ADC ch-1)
Efficiency and signal amplitude show a clear correlation
KLOE - 29 May 2003
Correlation also with our measurements after dismounting

## Slide 6
E. Santovetti
Time resolution for photons ~ 2.4 ns
Background and time resolution
Background occupancy ~ 0.3
( t = 200 ns, all QCAL)
Dt (ns)
(from KL  +-0 events)
in 10 ns background 1.5%
KLOE - 29 May 2003

## Slide 7
E. Santovetti
Electronic noise
EMC level
Unexpected electronic noise
very high
correlated with the machine RF
TDC and ADC affected
high frequency
KLOE - 29 May 2003
Pedestal sigma in ADC counts
ch. number
MIP ~ 200 ADC ch.
20 MeV photon ~ 50 ADC ch.
(depends on channel !)

## Slide 8
E. Santovetti
Old FE electronics scheme
KLOE S.C.- 29 May 2003
Amplifier 60 cm far from the PM base
No grounding shield oround the PM
amplifier
60 cm coax
12 m thin coax
SDS
PM not accessible

## Slide 9
E. Santovetti
Electronics changes
KLOE - 29 May 2003
Thin double electrical shield around the PM
Amplifier very close to the PM divider (10 cm of coaxial cable)
Differential amplifier to reduce the noise (receiver on a VME board in the SDS crate). Each amplifier in a small box removable.
Overall gain increased for a factor ~ 4x2 respect to the previous one.
twisted signal cables (shielded)
the worst 10 photomultipliers replaced
All the pieces are ready and tested
And have being mounted
amplifier
10 cm coax
12 m twisted
receiver
SDS

## Slide 10
E. Santovetti
Upgrade status
KLOE - 29 May 2003
All the PM’s, new dividers, cables and amplifiers are ready and tested.
As soon the machine group will finish his work on the IR, all this pieces will be mounted and tested on the apparatus (two weeks). At the and of the mounting and testing, we should care about the light tightness of the calorimeters and prepare them for the insertion
Receivers boards and low voltage dividers boards are now under mounting and will be tested and ready next week, in order to be placed on the detector in the first half of June